Server hardening

* Host Information
- Servername: lintiba
- Ip Address: 192.168.2.2
- Domain: ouedraogo.nl

* Hardening
N	Hardening	Config files	Comments	Completed
1	Configure the BIOS			X
2	Configure the BIOS	/etc/issue / /etc/motd	Copie the original cfg files into .orig. / Added the msg text into the cfg files .	V
3	Configure OpenSSH	/etc/ssh/sshd_config	Port 22222 / ListenAddress 0.0.0.0 / PermitRootLogin no / PasswordAuthentication no	V
4	Disable Ctrl+Alt+Tab	/etc/inittab/etc/init/ / control-alt-delete.override	Comment out the following in /etc/inittab out: / #start on control-alt-delete / #exec /sbin/shutdown -r now "Control-Alt-Delete pressed"	V
	Keep /boot as read-only	/etc/fstab	Linux kernel and its related files are in /boot directory which is by default as read-write. Changing it to read-only reduces the risk of unauthorized modification of critical boot files. To do this, open “/etc/fstab” file / /boot ext4 defaults,ro 1 2 / Please note that you need to reset the change to read-write if you need to upgrade the kernel in future.	V
5	Minimize Packages to Minimize Vulnerability	Run ntsysv cmd	This open a list of all services and you can easy check those that need to be enabed.	V
6	Turn Off IPv6	NETWORKING_IPV6=no / IPV6INIT=no	/etc/sysconfig/network	V

Source:
http://www.giac.org/registration/certified-unix-security-administrator-gcux
http://www.tecmint.com/linux-server-hardening-security-tips/